## Signal and data encoding
200318, updated 20.3.2020/pekka
An Android phone can only turn flash on or off, the shortest pulse which can be reliably generated is approximately 10ms. This is enough, amount of data to be transferred is small. Typically WiFi network name and password, and optionally some extra information.
### Zero and one bits
When sending Android’s LED keeps on turning on and off continuously. What matters is how long LED stays in same state: 10ms for “0” bit and 20 ms for “1” bit. So time between transitions matters, direction of transition is ignored. If doesn’t matter if LED switches from on to off or vice versa.

The Gazerbeam receiver is not very time critical, timing can be changed quite much and it should still work. Pulse length is recorded on fly and basic rule is that “1” must be clearly longer than “0”. Anyhow if taken very far from tested, the high pass filtering RC may need to be adjusted.
### From bits to messages
A message contains all data what user entered and is repeated endlessly: Android application doesn’t know when it is received by micro-controller.

- The message starts with 9 zero bits and then one bit, like “0000000001”.
- Then the 8 data bit for each data byte follow, least significant bit first. Add extra 1 bit is to each data byte, or 0 bit for last data byte. This data can never form nine consequent zeros (except for the last byte) and can be separated from beginning of message. Like “010010101”.
- There is no message length, extra bit 0 after data byte indicates end of message. Previous message is processed when a new message begins, at that point the previous message is considered “ready”.
- First two data bytes contain always checksum (MODBUS CRC), less significant byte first.
### Message content - fields
The message starts with two byte checksum. This needs to be generated by Android code, and is checked and stripped away by the Gazerbeam library.

Following the check sum there are 1 or more fields:
- A field starts with field id byte.
- Next byte is field data length, specifies number of data bytes.
- N data bytes

The field IDs are (list here)