# Introduction
200318, updated 20.3.2020/pekka
The “gazerbeam” library enables configuring microcontroller’s WiFi network name (SSID) and password (PSK) using LED flash of Android phone, etc.
- The phone needs APP to blink configuration information, example Android Java application named “blinky” is in iocom/extensions/gazerbeam/examples/blinky directory.
- A photo transistor is connected to microcontroller tough electronics for it to receive the signal.
- Microcontroller gets signal from electronics as digital input. It is set up so that changes to the signal trigger interrupt. Gazerbeam library handles this and converts it to message.
- The transferred data is encoded into light signal using short and long intervals between loght on/off changes