## Signal encoding
200318, updated 20.3.2020/pekka
Standard Android phone can only turn flash on or off, and not control it’s intensity. It is also relatively slow, shortest pulse which can be reliably generated is approximately 10ms. Luckily for this application this is enough, amount of data to be transferred is small, typically WiFi network name and password, and optionally some extra information. Once wifi connection is establised, all data is transferred trough that.

When sending Android’s LED keeps on turning on and off continuously. What matters is how long LED stays in same state: 10ms for “0” bit and 20 ms for “1” bit. So time between transitions matters, direction of transition is ignored. If doesn’t matter if LED switches from on to off or vice versa.

A message contains all data what user entered and is repeated endlessly: Android application doesn’t know when it is received by micro-controller.

- The message starts with 9 zero bits and then one bit, like “0000000001”.
- Then the 8 data bit for each data byte follow, least significant bit first. An extra 1 bit is always appended to end. This data can never form nine consequent zeroes and can be separated from beginning of message. Like “010010101”.
- There is no message length, nor end of message mark. Just when new message begins, the previous message is considered “ready”.
- First two data bytes contain always checksum (MODBUS CRC), less significant byte first.