# Introduction
190527, updated 22.10.2019/pekka
The IOCOM library implements communication between a control computer and IO devices over TCP network or full duplex serial communication wire. The library supports scalable range of functionality. Minimum configuration supports only serial communication on plain metal, while some applications may require multi-threading and secured communication over Internet.

Micro-controllers can be used as plain metal, or equipped with Arduino derived libraries, FreeRTOS (currently testing), LWIP/W5500 for networking, and TLS library. The IOCOM is not bound tightly to any underlying system, so it can be ported basically to any environment with sufficient resources for the task. Still, using configuration which has been implemented and tested makes things much easier.

The same code runs on Windows and Linux. Linux on should cover Raspberry PI and similar devices. We are considering MAC and Android testing as well.

Communication security is becoming paramount in IoT and Manufacturing environments. Thus TLS integration, strong encryption and device identification are essential part of the project.
## Scaling from communication between two devices to secure IoT
At simplest IOCOM can be used as serial communication protocol between two devices. This doesn’t need to do with named register maps, network topology, security, etc. Then when we want to scale up to IoT with secured communication and connect trough shared server in cloud, we need to keep adding complexity.

Operating system abstraction layer capabilities can be turned on or off at eosal compile time by preprocessor defines. These include support for serial ports, TCP sockets, TLS, blue tooth, multi threading, persistent storage, etc. For example to build minimalistic support which can run on Arduino UNO, we would most likely to turn off everything but serial port.

The base iocom library is simple and small. The advanced features are implemented as extension libraries, which can be added as needed.